SenseView P430

User Guide

HIMS Co., Ltd.

TEL: +82 42 864 0133

FAX: +82 42 864 4462

E-mail: hims@himsintl.com

http://www.himsintl.com

TABLE OF CONTENTS

1. The P430 Package	2

2. Battery use / Maintenance	2

3. Buttons and Operation	4

4. Power saving mode	8

5. Battery indicator icon	9

6. On and off beep sound	11

7. Specification	11

8. Warranty	12

9. An FCC warning	13

1. The P430 Package

  - P430.

  - AC Power Adaptor.

  - User Guide.

  - Bag

  - Strap.

2. Battery use / Maintenance

- Battery must be fully charged for approximately 3 hours prior to initial use. Please connect the supplied AC Power Adapter to DC-input in order to charge the battery.

- Before using this unit, please remove the protection sheet on the LCD.

- To avoid electric damage, please use only the supplied AC Power Adaptor.

- To prevent fire or shock hazard, do not expose this unit to water or moisture.

- Please do not disassemble. Please refer servicing to qualified service personal only.

- After 6 months usage, the lifespan of the battery may be shortened.

- The default values;

The default values are being memorized and considered as the latest values (color, zoom, brightness) which are set lately, when the user sets the unit recently prior to the power off. When switching on again, the latest setting values are being restored and operated as the latest setting values.

3. Buttons and Operation

< Explanation of each button on all the panels >

- Power on/off switch: Please slide down and release this switch in order to turn power on or off. When the unit is turned on, it displays “logo” on the screen for about 2 seconds, and then it turns in magnification mode.

- Zoom button: By pressing zoom in/out (+/-) button, you can control magnification rate in step 1-9.

Zoom ratio

| step | Legs unfolded | Legs folded up |
| --- | --- | --- |
| 1 | 4.7 | 6.7 |
| 2 | 6.0 | 8.0 |
| 3 | 6.8 | 9.5 |
| 4 | 8.4 | 11.6 |
| 5 | 9.5 | 13.0 |
| 6 | 10.3 | 13.6 |
| 7 | 11.9 | 15.8 |
| 8 | 13.6 | 19.0 |
| 9 | 15.8 | 22.5 |

- Still image button: Please press the button and images are to be frozen. Please press the button again to exit the still image mode.

- Camera indicator: It indicates the camera lens position. This indicator blinks while in power save mode. (Power saving mode will be explained on Section 4 in this user manual)

- Brightness button: Adjust brightness for the darker and lighter images on the LCD screen with brightness button from level 1 to level 4. If you press the button again at level 4, it returns to in level 1.

- External video input: This is input for an external camera supplied as option.

- Color mode button: Pressing this button will change the color on the display. There are 6 color modes as follows.

(1) Full color mode.

(2) Black on white mode.

(3) White on black mode.

(4) Yellow on blue mode.

(5) Blue on yellow mode.

(6) Blue on white mode.

If you press the button again at mode 6, it returns to mode 1.

- DC-input: To keep an internal battery 100% charged, plug AC Power Adapter in this DC-input.

- Sliding handle: Please pull out the sliding handle to prevent any interruptions that the camera can be hidden by your hand.

- Hole for strap: This is the hole to connect strap.

4. Power saving mode

- If users leave this unit turned on and do not move the unit for 3 minutes, power saving modes is activated. At the power saving mode, backlight of the LCD is turned off and camera indicator blinks.

- To exit from power saving mode, simply press any button or let the unit move.

- If users leave the unit for 7 more minutes after starting up the power saving mode, the power will be turned off automatically. If you need to use again, you should turn on the power switch.

- During still image is displayed on the LCD and the unit does not move for more than 10 minutes, the power will be turned off automatically.

5. Battery indicator icon

    - The battery indicator icon is displayed at up right corner on the LCD screen. It indicates state-of-charge. If the battery is needed to recharge, the battery indicator icon blinks.

    - Please press both Color Mode button and Zoom Out (-) button simultaneously and you get the battery indicator icon on the LCD screen. If you press both buttons again, the battery icon will disappear.

    - The battery indicator icon is red color when this unit is being recharged by connecting AC Power Adapter to the DC-input. When the unit is fully charged, the color of the battery indicator icon is changed to green.

* Even though the battery icon is changed to green color, please keep the AC Power Adapter plugged in for a couple of hours

    - If the AC Adapter is plugged out from the unit, the color of battery indicator icon is changed to blue color.

6. On and off beep sound

- Whenever the button is pressed, it sounds beep.

- Pressing Zoom In (+) button and Brightness buttons simultaneously will turn on or off this beep sound.

7. Specification

  - LCD window size: 4.3 inch Wide QVGA TFT-LCD (16:10 wide).

  - Zoom: x4.7 ~ x22.5.

  - Brightness: level 1 to 4.

  - Color: 6 color modes.

Full color / Black on white / White on black / Yellow on blue / Blue on yellow / Blue on white.

  - External video input.

  - Battery type: Rechargeable lithium polymer.

      - Battery Operational time: 5 hours.

      - Recharge time: 3 hours.

  - Sliding handle.

  - Dimension: 83(W) x 146(D) x 22.5(H) mm. (25(H) mm, Legs unfolded).

  - Weight: 221g.

8. Warranty: 1 year (except for battery)

9. An FCC warning

NOTE: This equipment has been tested and found to comply with the limits for a Class B digital device, pursuant to part 15 of the FCC Rules. These limits are designed to pro-vide reasonable protection against harmful interference in a residential installation.

This equipment generates, uses and can radiate radio frequency energy and, if not in-stalled and used in accordance with the instructions, may cause harmful interference to radio communications. However, there is no guarantee that interference will not occur in a particular installation. If this equipment does cause harmful interference to radio or television reception, which can be determined by turning the equipment off and on, the user is encouraged to try to correct the interference by one or more of the following measures:

-Reorient or relocate the receiving antenna.

-Increase the separation between the equipment and receiver.

-Connect the equipment into an outlet on a circuit different from that to which the receiver is connected.

-Consult the dealer or an experienced radio/TV technician for help.

CAUTION : Changes or modifications not expressly approved by the manufacturer responsible for compliance could void the user’s authority to operate the equipment.

# Text boxes

E.

F.

I.

C.

H.

D.

A.

B.

J.

G.